## Slide 1: Penetration Resolution in Computer Modeled Fabrics
Collin Blake
Dr. John Whitcomb

## Slide 2: Outline
Background
  Textile Simulation
  Data Types
Problem
ideas
Solution 1
Solution 2
SISL Library
Solution 3
  Separating Axis Theorem
Issues
Current Work
Future Plans

## Slide 3: Background
Evolution of composite materials lead into computational analysis and design of fiber-reinforced structures
Current focus of these materials is understanding and simulating damage initiation and propagation
Extensive research at microstructure level
Mesoscale next level

## Slide 4: Background
Evolving modelling techniques and computational ability allow us to model increasingly complex geometries for computer analysis
Modelling discrete fibers very computationally expensive
Using Homogenized Tows with matrix surrounding tows

## Slide 5: Textile Simulation
Using VTMS
Digital chain method to generate realistic woven geometry
Discrete fiber filaments can then be converted into homogenized tows and modelled in a matrix
Creates realistic woven geometries that can be analyzed

## Slide 6: Data Types of VTMS
Standard Tow Format
Stacks that describe tow cross-section along tow path, defined by nodes
Internally, node location and outward normal stored, along with stack ownership
Exported data described by stack, with each node belonging to said stack

## Slide 7: Data Types of VTMS (cont’d)
Clipped Tow Format
More traditional surface mesh style with surface elements and nodes
Internally stored is node location, element connectivity, and element outward normal
Exported data translates this data well
Currently do not have visualization tool implemented

## Slide 8: Penetration
Created geometries come with penetrating surfaces
  Tows in close proximity develop surface penetrations after tow surface creation
  Detecting Penetrations main problem
Conventional FEA programs cannot run analysis

## Slide 9: Ideas
Polyhedron Penetration Detection
  Used in video game physics
  Difficult to determine penetration distance
  Used primarily as avoidance, not resolution (time dependent)
  Involves bounding box or Separating Axis theorem
  Can also use node to surface distance and orientation algorithms to determine penetrating surface nodes
Use NURBS Surface to define penetrating surfaces
  Gives analytical solution
  More accurate for allowing intersection curves vs. penetrating nodes
  Defines Penetration surface boundary
  Reduces tow volumes during fitting
  Can be difficult to redefine tow mesh along boundary

## Slide 10: Initial Solution
In order to impose surface to surface contact, a plane is placed between the penetrating surfaces.
The penetrating nodes are then moved to this surface
This will ideally create a perfect contact surface between the tows

## Slide 11: Issues Encountered
Creates “Spurs” near penetration boundary
Does not account for large curvatures
Can create too large of surface, significantly altering tow topography
Matrix pockets can also occur

## Slide 12: Solution 2
Find nearest neighbor of penetrating node on tow being penetrated
Compute half distance and move both nodes to location
Resolves compatibility

## Slide 13: Solution 2 (cont’d)

## Slide 14: Solution 2 (Cont’d)
Known Issues
  Degenerate Elements
  Nodes allowed to move outside tow boundary
  Jagged topography between tows
Possible Solutions
  Mesh cleaning to renumber elements and nodes
  Improve penetration routines
  Correct with smoothening

## Slide 15: SISL Library
Non-Uniform Rational B-Splines software library that gives user multiple algorithms for defining, using, and performing operations on surfaces
Interested in ability to describe discrete surfaces as analytic description and evaluate intersection between two surfaces
We would use this intersection data to create a solution to resolve penetration boundaries

## Slide 16: Solution 3
Create NURBS representation of tow surface using SISL library and .stw format (exported standard tow)
Continue to use library to detect interpenetration regions in the form of curves that encase the penetrations
Use these curves to correct the interpenetrations
Once the curves are found, the surfaces are translated back to a discrete surface mesh by sampling the NURBS surface and creating triangular elements

## Slide 17: Solution 3 (Cont’d)
Once we have boundary curves, we translate the boundary curve into linear piecewise elements
We can use these piecewise curves to then verify that the curves are unique and do not overlap
An algorithm does this by determining if the endpoints of an curves lie on another
If this is the case we combine the curve unless they are duplicates, in which case we throw one away

## Slide 18: Separating Axis Theorem
The Separating Axis Theorem (SAT) is used to identify if two shapes (or line segment) intersect
It starts by selecting axes to project the limits of the shapes onto
  Usually the chosen axes are those that are perpendicular to the edge of shape
Then the projections are tested to verify if they overlap
  Overlap means they intersect
There only needs to be one axis on which the projections do not overlap to say that the shapes do not intersect

## Slide 19: Solution 3 (CONT’d)
Using the unique curves, we loop over each curve segment and use a KDTree to find the nearest surface elements to the segment for both tows
Then for each element we check that the segment intersects or not using the Separating Axis Theorem
If the segment intersects the element, we store the element and then check if an element edge is intersected by the segment
  If so, the segment is divided by a point that identifies where the edge and segment cross

## Slide 20: Solution 3 (Cont’d)
Once all elements of both tows have been looped over, we return the intersected elements and the refined intersection boundary curve
Then we loop over the intersected elements and for each element we determine if a segment has a node in or lies on the edge of an element
We collect the nodes and through an algorithm
Then sub-mesh the element using the boundary segment points and intersection points

## Slide 21: Solution 3 (Cont’D)
Once every intersected element is sub-meshed, we add the new sub-meshes back to the surface mesh
  Have also attempted to reduce curve refinement by only keeping one node between intersection points
  Or less
The result is surface tow meshes that are compatible along the boundary curves

## Slide 22: Issues
One of the biggest issues currently is the high aspect ratio elements and uneven, high refinement areas of sub-meshed elements
Occurs:
  When boundary curve is close to element node
  When two intersection points from different tows are close
Possible solutions:
  Move element node to intersection point, effectively removing the penetration

## Slide 23: Current Work
Solving issue of “bad” element refinement
  As discussed, high-aspect elements cause numerical issues
  Possible solutions still being explored
Collecting of elements contained by boundary curves after refinement
  Analyzing implementation of current algorithms for determining outward normal of surface elements
  Could significantly speed up collection algorithm

## Slide 24: Future Work
Finish element gathering inside of boundary curve
Implement Boolean operation for adding/subtracting meshes between tow surfaces
Create output format for interpenetration elements and visualization tools
Discuss further improvements if time permits

## Slide 25
Questions?

## Slide 26: NURBS

## Slide 27: K-D Tree