## Slide 1: Modeling CMC Microstructures Using Segmented Fiber Data
Collin Blake
Contractor
AFRL/RXCC
Air Force Research Laboratory

## Slide 2: Motivation
Desire to better understand microstructure and its effects on material properties at macro scale
Quantify structure properties that induce and drive damage within microstructures
Create a database of reoccurring micro structures with high damage probabilities
Difficulties
Combining coatings and separation of clusters in BSAM
Accurate and robust surface selection algorithm
Proper mesh seeding/size
Optimization with respect to time

## Slide 3: Background
Matlab script that gives geometric fiber data (i.E. X- and y-coordinates, major and minor axis, angle of rotation, etc.) From fiber-matrix scan
Need to produce a model that can be executed using BSAM

## Slide 4: Segmentation and Division
Analyze one layer at a time, using Matlab script to identify and describe fibers
Data is then divided into sub-sections using a separate Matlab script file

## Slide 5: Modeling
Start with coordinates and radius of each fiber (idealized model)
  Data given in elliptical format, for now we assume idealized circles
  Assumption is due to image given has angled fiber orientation, therefore radius should be minor axis of fibers given
Using Abaqus with a Python script file, coatings are added and combined
  Difficulties arise for combining coatings
  Discussion in next slide

## Slide 6: Combining Coatings
Single cluster for all coatings
  Combine geometries at sketch level
  Using circle intersection formula to find intersection points and create arcs
Single cluster per coating
  Combine geometries at the part level
  Simple Boolean command in Abaqus with renaming of part instance

## Slide 7: Modeling (cont’d)
An assembly is created to mesh
  Matrix template is created and is then cut by fiber and coatings
  Assembly is then created by inserting part instances into the assembly for meshing
  Complex geometries require mesh refinement around intersections

## Slide 8: Modeling
Start with coordinates and radius of each fiber (idealized model)
  Assume radius is the minor axis, eccentricity to be added later
  Fibers are not allowed to overlap
Using Abaqus with a Python script file, coatings are added and combined
  Coatings as a single cluster leads to suppression of crack insertion
  Later changed to separate clusters for crack initiation
An assembly is created to mesh
  Refinement of seed to ensure matrix meshing and mesh compatibility
Single cluster for all coatings
Individual cluster for each coating

## Slide 9: Meshing Geometries
Complex geometries require mesh refinement around intersections
  Sharp points are created from intersection of coatings
  High refinement needed in this area to mesh without error
  Will look for better refinement options in the future

## Slide 10: Surface Selection
In order to use BSAM connection properties for interfaces, connecting surfaces must be found
  Use bounding cylinder around coating node to select nodes in matrix that correlate to nodes on each coating
  Take found nodes and determine connecting elements
  Save found elements for connection element sets in BSAM

## Slide 11: Modeling (cont’d)
Resulting mesh is saved in Abaqus
In order to use BSAM connection properties for interfaces, connecting surfaces must be found
Surface selection is much more difficult for individual coatings

## Slide 12: Input and Analysis
Once connections are established, an input file is created and then run using BSAM
  File includes output for loading along boundary conditions for load-displacement curves
  Allows for Mesh Independent cracking along with separation between interfaces
  Looking for modes of damage propagation

## Slide 13: Currently
Reworking selection algorithms for efficiency and speed
  Implementation of advanced searching algorithms and rewrite of output portion of script
Modifying surface selection for robustness
  Additional consideration for fiber connection orientations and patterns
Finalizing modifiable parameters and callable arguments
  Includes thickness, separation factor for fibers, and mesh seed value

## Slide 14: Future Tasks
Further improve fiber identification method and speed of model creation further
Collect numerical data from simulations and being quantitative characterization
Add ability to have eccentricities in coatings, fiber shape, and possible void insertion
Create macro to fully compile models for all sub-sections in a given picture larger than one layer

## Slide 15
Questions?